## Slide 1: SERVERLESS IOT DATA PROCESSING

## Slide 2
#include <ESP8266WiFi.h>
#include <DHT.h>
char ssid[] = "your_SSID";
char pass[] = "your_PASSWORD";
#define DHTPIN D1
#define DHTTYPE DHT11
DHT dht(DHTPIN, DHTTYPE);
void setup() {
Serial.begin(115200);
WiFi.begin(ssid, pass);
while (WiFi.status() != WL_CONNECTED) {
delay(1000);
Serial.println("Connecting to WiFi...");
}

## Slide 3
Serial.println("WiFi connected");
pinMode(D2,OUTPUT); // BULB
pinMode(D3,OUTPUT); // FAN
pinMode(D6,OUTPUT); // KITCHEN
pinMode(D7,OUTPUT); // AC
pinMode(D4,OUTPUT); // TV --R
digitalWrite(D2,LOW);
digitalWrite(D3,LOW);
digitalWrite(D6,LOW);
digitalWrite(D7,LOW);
digitalWrite(D4,LOW);
dht.begin();
}

## Slide 4
void loop() {
float h = dht.readHumidity();
float t = dht.readTemperature();
if (isnan(h) || isnan(t)) {
Serial.println("Failed to read from DHT sensor!");
} else {
Serial.print("Humidity: ");
Serial.print(h);
Serial.print(" %\t Temperature: ");
Serial.print(t);
Serial.println(" *C");
if (t > 25.0) {
digitalWrite(D2, HIGH); // Turn on the bulb
} else {
digitalWrite(D2, LOW); // Turn off the bulb
}
}
delay(2000);
}

## Slide 5
Include Libraries:
#include <ESP8266WiFi.h>: This includes the library necessary for Wi-Fi communication with the ESP8266.
#include <DHT.h>: This includes the library for interfacing with the DHT temperature and humidity sensor.
Wi-Fi Credentials:
char ssid[] = "your_SSID"; and char pass[] = "your_PASSWORD";: You need to replace "your_SSID" and "your_PASSWORD" with your actual Wi-Fi network name (SSID) and password.
Pin Definitions:
#define DHTPIN D1: Defines the digital pin to which the DHT sensor is connected.
#define DHTTYPE DHT11: Specifies the type of DHT sensor being used (DHT11 in this case).

## Slide 6
DHT Sensor Initialization:
DHT dht(DHTPIN, DHTTYPE);: This initializes the DHT sensor on the specified pin.
Setup Function:
Serial.begin(115200);: Starts serial communication for debugging at a baud rate of 115200.
WiFi.begin(ssid, pass);: Attempts to connect to the Wi-Fi network using the provided credentials.
The while loop waits until a successful connection is established.
Once connected, it prints a message indicating successful connection.
Device Pin Configuration and Initialization:
pinMode(D2, OUTPUT); to pinMode(D4, OUTPUT);: Sets the specified pins as output for controlling devices (bulb, fan, etc.).
digitalWrite(..., LOW);: Initially turns off all devices.

## Slide 7
DHT Sensor Initialization:
dht.begin();: Initializes communication with the DHT sensor.
Loop Function:
The loop function repeatedly performs the following tasks:
Reads the humidity and temperature from the DHT sensor.
Checks if the readings are valid (not NaN, which indicates a sensor reading failure).
If the readings are valid, it prints them to the serial monitor.
It then checks the temperature reading and controls the bulb based on a condition. In this example, if the temperature is greater than 25.0°C, it turns on the bulb; otherwise, it turns it off.